## Slide 1
TITLE Product disassembly
The learning intent.
To explain engineered products functions, properties and suitability for use.
Why are we learning this? To analyse existing products as part of your controlled assessment
SUPPORT
What is it made from? What properties does this have? Why is it made from this material?
VCR Keywords – properties, functions, performance
Explain components of engineered products to evaluate properties and material suitability.
Description of components of engineered products to evaluate properties and material suitability.
.The success criteria.
Identification of components of engineered products to evaluate properties and material suitability.
PASS
MERIT
DISTINCTION

## Slide 2
Make notes on all of the parts.
Eg.
Outer buttons: Mechanical component.
Made of ABS because it is durable and has elasticity so that the electronic buttons can be pressed.
injection moulded because it is a complicated shape.
Curved shape to be ergonomical and to continue the shape of the whole mouse.
Use the help on the next 3 pages.
Task 1: Key Features and Spec
Slide 2

## Slide 3
TASK
Identify the key features and functions required from the information provided. Use this information to develop a design specification.
Identifying key features and functions E.g.
Injection molded product
Holds up to 8 batteries
Charges AA & AAA Batteries
Does not charge PP3, C or D
It charges Ni-Mh or NiCd Batteries
It’s double insulated
Has no metal earth pin
Has a CE mark
Runs on 240v
Has a brand logo on the base
The brand is a registered trademark
Front & back are labeled
There are two LED’s to show charge
Positive & negative clearly shown
Springs are used to hold in battery
Springs also conduct the current
There are 8 springs
There are grooves on the top to improve aesthetic appeal
There are two main mold components
Both parts are a different colour
There are four fixing screws.
These screws are machine screws
Earth, live and neutral are marked on thecase
There is a British Standard number
Recycling information is present
Indoor use symbol is present
Maximum battery capacity is shown
There is a PCB inside to control current
The PCB is held in place on 4 bosses
There are 4 webs to increase strength
The fixing screws pass through bosses
Insulated cable runs to the springs
The PCB has capacitors & resistors
The threads are cut into the casing
The live and neutral pins are partly shielded
There is a model number
There is a flat base to allow it to stand
The case is smooth
All edges have a radius
The form allows batteries to be easily taken out
The product costs £15.00
It is 100 mm high 500 deep and 40 mm wide
It weighs 200 grams
The logo is red so it stands out
The LED’s are red when charging
There is a hole to see the rear batteries
REQUIREMENTS (that meet a brief)
Aesthetics
Environment
User/Customer/Client
Cost
Safety
Ergonomics
Size
Limits
Sustainability
Example

## Slide 4
  ABS Buttons- make the small electronic buttons larger… Why is this important?

## Slide 5
  ABS Casing top– Holds and protects the battery and circuit? Why is this important?

## Slide 6
ABS Casing bottom. Slides easily on a table - How and why is this important?

## Slide 7
Acrylic Optical sensor casing -Holds the sensor in place- Why is this important?

## Slide 8
Rubber wheel - Turns the forward and backward. Why is this important? How is it sensed?

## Slide 9
  Electronic Buttons – How do they pick up movement from the big buttons?

## Slide 10
  Screws- Hold the mouse together. Why is this important ?

## Slide 11
SMT (surface mount technology) Circuit Board- Uses the battery's to light up the LED and power the circuit. Why is this important?

## Slide 13
https://www.youtube.com/watch?v=lK3RFd6EBp8